## Slide 1
m.gutierrez-pozo@cranfield.ac.uk
Volatile fingerprinting of potato rots during cold storage
QCAP
Background
Identification of potato rots Volatile Organic Compound (VOC) – biomarkers for the development of a low cost, compact and sensitive multi-species trace gas sensor for the early detection of potato diseases under commercial storage conditions.
Determine the pathogen-specific VOCs released by the potato and the pathogen.
Aim and objective
Potato is one of the main food crops in the world. Half of the potato crop is stored for up to 12 months
Potato storage is a dynamic process where environmental conditions must be able to react to changes by the optimization of the conditions during the storage
Environmental conditions
T (4-10oC)
R.H (90-100%)
Fungal and bacterial growth on potatoes. Potato storage diseases are acquiring more and more importance due to the increased demand of the pre-process potato market
Wrong or insufficient management of storage conditions
Requirement
Perfect skin finish without any blemishes
Retail or processing
Early identification of potato rots
Potato spoilage and waste
Methodology
The three main diseases that affected potato tubers in the last year; soft rot (Pectobacterium carotovorum atrosepticum), dry rot (Fusarium solani coeruleum) and gangrene (Boeremia foveata) have been studied. VOCs have been analysed by Thermal Desorption-Gas Chromatography-Time of Flight-Mass Spectrometry (TD-GC-ToF-MS) under laboratory conditions, while the developed sensor will be used under commercial conditions.
Potato surface sterilisation
Potato inoculation
Potato incubation
VOC sampling with Thermal Desorption tubes (TD)
Analysis & VOC identification
TD-GC-ToF-MS
Trace gas sensor
Results
Maria Gutiérrez-Pozo, Fernando Rubio-López, Leon Terry, Sofia Kourmpetli & Ángel Medina
Volatile Organic Compound biomarkers search was carried out by comparing the chromatograms resulted from VOC sampling of non-infected potato tubers with those infected with the different pathogens. Figure 1 shows an example of the different VOC profiles of non-infected potato tubers (Fig.1a) and Pectobacterium - infected ones (Fig.1b). Current work is being focused on the identification of possible biomarkers based on the presence and abundance of characteristic VOCs on the samples from infected tubers. This data will be used for the development of a low cost, sensitive, multi-species trace gas sensor.
a
b
Methylene chloride
Methylene chloride
Methyl ester acetic acid
Methyl ester acetic acid
3-methyl pentane
2-methyl butane
3-methyl pentane
2-methyl butane
Figure 1. Chromatograms resulted from VOC sampling of a. non-infected potato tubers and b. potato tubers infected with Pectobacterium carotovorum atrosepticum.